COMPANY IDENTITY:  Cascade Designs, INC.			DATE: 08/16/04

PRODUCT IDENTITY:  MSR Superfuel  				PAGE 1 OF 7

REVISION DATE: 11/02/2004                                 SUPERCEDES: 11/28/2001?

MATERIAL SAFETY DATA SHEET

This Material Safety Data Sheet conforms to the requirements of ANSI Z400.1.

THIS MSDS COMPLIES WITH 29 CFR 1910.1200 (HAZARD COMMUNICATION STANDARD)

IMPORTANT: Read this MSDS before handling & disposing of this product.

Pass this information on to employees, customers, & users of this product.

SECTION 1. IDENTIFICATION OF THE SUBSTANCE/PREPARATION AND COMPANY

PRODUCT IDENTITY: MSR Superfuel

COMPANY IDENTITY: CASCADE DESIGNS, INC.

COMPANY ADDRESS:  4000 1st Ave. South

COMPANY CITY:     SEATTLE, WA 98134

COMPANY PHONE:    1-206-505-9500

CHEMTREC PHONE:   1-800-424-9300

SECTION 2. COMPOSITION/INFORMATION ON INGREDIENTS

CONTAINS:	95-100% LIGHT HYDROTREATED DISTILLATE (68410-97-9)[270-093-2]

Number in parentheses is CAS #, number in brackets is European EC #.

LF0001                  SECTION 3. HAZARDS IDENTIFICATION

RISK STATEMENTS:

R11          Highly Flammable.

R18          In use, may form flammable/explosive vapor-air mixture.

R65          Harmful: may cause lung damage if swallowed.

R36/37/38    Irritating to eyes, respiratory system and skin.

R20/65       Harmful by inhalation, may cause lung damage if swallowed.

SAFETY STATEMENTS:

S9           Keep container in a well-ventilated place.

S16          Keep away from sources of ignition. No smoking.

S26          In case of contact with eyes, rinse immediately with

plenty of water and seek medical advice.

S45          In case of accident, or if you feel unwell, seek medical advice

immediately. (Show the label where possible).

S53          Avoid exposure - Obtain special instructions before use.

COMPANY IDENTITY:  Cascade Designs, INC.			DATE: 08/16/04

PRODUCT IDENTITY:  MSR Superfuel  				PAGE 2 OF 7

REVISION DATE: 11/02/2004                                 SUPERCEDES: 11/28/2001?

SECTION 4. FIRST AID MEASURES

EYE CONTACT:

For eyes, flush with plenty of water for 15 minutes & get medical attention.

SKIN CONTACT:

In case of contact with skin immediately remove contaminated clothing.

Wash thoroughly with soap & water. Wash contaminated  clothing before reuse.

INHALATION:

After high vapor exposure, remove to fresh air. If breathing is difficult,

give oxygen.  If breathing has stopped give artificial respiration.

SWALLOWING:

If swallowed, CALL A PHYSICIAN IMMEDIATELY! Do NOT induce vomiting. Have

patient lie down & keep warm.  Vomiting may lead to pneumonitis, which may

be fatal.

LF0001                  SECTION 5. FIRE FIGHTING MEASURES

EXTINGUISHING MEDIA

NFPA Class B extinguishers (Carbon Dioxide or foam)for Class I B liquid fires.

SPECIAL FIRE FIGHTING PROCEDURES

Water spray may be ineffective on fire but can protect fire-fighters

& cool closed containers. Use fog nozzles if water is used.

Do not enter confined fire-space without full bunker gear.

(Helmet with face shield, bunker coats, gloves & rubber boots).

Use NIOSH approved positive-pressure self-contained breathing apparatus.

UNUSUAL EXPLOSION AND FIRE PROCEDURES

EXTREMELY FLAMMABLE!! VAPORS CAN CAUSE FLASH FIRE

Keep container tightly closed.

Isolate from oxidizers, heat, sparks, electric equipment & open flame.

Closed containers may explode if exposed to extreme heat.

Applying to hot surfaces requires special precautions.

Empty container very hazardous! Continue all label precautions!

SECTION 6. ACCIDENTAL RELEASE MEASURES

CONTAINMENT TECHNIQUES

Stop spill at source. Dike area & contain.

CLEAN-UP PROCEDURES:

Clean up remainder with absorbent materials. Mop up & dispose of. Persons

without proper protection should be kept from area until cleaned up.

OTHER PRECAUTIONS

Vapors may ignite explosively & spread long distances. Prevent vapor buildup.

Put out pilot lights & turn off heaters, electric equipment & other

ignition sources during use & until all vapors are gone.

COMPANY IDENTITY:  Cascade Designs, INC.			DATE: 08/16/04

PRODUCT IDENTITY:  MSR Superfuel  				PAGE 3 OF 7

REVISION DATE: 11/02/2004                                 SUPERCEDES: 11/28/2001?

SECTION 7. HANDLING AND STORAGE

HANDLING

Isolate from oxidizers, heat, sparks, electric equipment & open flame.

Use only with adequate ventilation. Avoid breathing of vapor or spray mist.

Avoid contact with skin & eyes.

Wear OSHA Standard goggles or face shield. Consult Safety Equipment Supplier.

Wear gloves, apron & footwear impervious to this material. Wash clothing

before reuse.

Avoid free fall of liquid. Ground containers when transferring. Do not flame

cut, saw, drill, braze, or weld. Empty container very hazardous! Continue

all label precautions!

STORAGE

Vapors may ignite explosively & spread long distances. Prevent vapor buildup.

Put out pilot lights & turn off heaters, electric equipment & other

ignition sources during use & until all vapors are gone.

Do not store above 49 C/120 F. Store large amounts in structures made for

OSHA Class I B liquids. Keep container tightly closed

& upright when not in use to prevent leakage.

LF0001          SECTION 8. EXPOSURE CONTROLS/PERSONAL PROTECTION:

RESPIRATORY EXPOSURE CONTROLS

A respiratory protection program that meets OSHA 29 CFR 1910.134 and

ANSI Z86.2 requirements or European Standard EN 149 must be followed

whenever workplace conditions warrant a respirator's use.

VENTILATION

LOCAL EXHAUST                         : Necessary

MECHANICAL (GENERAL)                  : Acceptable

SPECIAL                               : None

OTHER                                 : None

PERSONAL PROTECTIONS:

Wear OSHA Standard goggles or face shield. Consult Safety Equipment Supplier.

Wear gloves, apron & footwear impervious to this material. Wash clothing

before reuse.

WORK & HYGIENIC PRACTICES:

Provide readily accessible eye wash stations & safety showers.

Wash at end of each workshift & before eating, smoking or using the toilet.

Promptly remove clothing that becomes contaminated. Destroy contaminated

leather articles. Launder or discard contaminated clothing.

COMPANY IDENTITY:  Cascade Designs, INC.			DATE: 08/16/04

PRODUCT IDENTITY:  MSR Superfuel  				PAGE 4 OF 7

REVISION DATE: 11/02/2004                                 SUPERCEDES: 11/28/2001?

SECTION 9. PHYSICAL DATA

APPEARANCE :                                          		Liquid,Water-White

ODOR :                                                		Mild

BOILING RANGE :                   			 52 110 137 C / 125 231 280 F

AUTO IGNITION TEMPERATURE :                	321 C /  610 F  (Lowest Component)

LOWER FLAMMABLE LIMIT IN AIR (% by vol):     				  1.9

FLASH POINT (TEST METHOD):            					-18 C / -2 F (TCC)

FLAMMABILITY CLASSIFICATION: 						Class I B

GRAVITY @ 60 F :

API :                                                  	 70.6

SPECIFIC GRAVITY (Water=1) :                            	  0.700

POUNDS/GALLON :                                        	  5.831

VOC'S (>0.44 Lbs/Sq In) :           100.0 Vol. % /   700.0 g/L / 5.831 Lbs/Gal

TOTAL VOC'S (TVOC) :                100.0 Vol. % /   700.0 g/L / 5.831 Lbs/Gal

NONEXEMPT VOC'S (CVOC) :            100.0 Vol. % /   700.0 g/L / 5.831 Lbs/Gal

HAZARDOUS AIR POLLUTANTS (HAPS) :     0.0  Wt. % /     0.0 g/L / 0.000 Lbs/Gal

VAPOR PRESSURE (mm of Hg)@20 C                           		150.0

NONEXEMPT VOC PARTIAL PRESSURE (mm of Hg @ 20 C)         		150.0

VAPOR DENSITY (air=1) :                                    	  2.4

WATER ABSORPTION :                                    		Negligible

REFRACTIVE INDEX :                                       		  1.357

SECTION 10. STABILITY & REACTIVITY

STABILITY

Stable under normal conditions.

CONDITIONS TO AVOID

Isolate from oxidizers, heat, sparks,  electric equipment & open flame.

MATERIALS TO AVOID

Isolate from strong oxidizers such as permanganates,chromates & peroxides.

HAZARDOUS DECOMPOSITION PRODUCTS

Carbon Monoxide, Carbon Dioxide from burning.

HAZARDOUS POLYMERIZATION

Will not occur.

LF0001                SECTION 11. TOXICOLOGICAL INFORMATION

MATERIAL                                CAS #    TWA (OSHA)    TLV (ACGIH)   HAP

LIGHT HYDROTREATED DISTILLATE         68410-97-9    500 ppm     300 ppm     No

In addition to EPA Hazardous Air Pollutants showing `Yes' under "HAP" above,

using manufacturers' data, based on EPA Method 311, the following EPA

Hazardous Air Pollutants may be present in trace amounts (less than 0.1%):

Benzene,Polycyclic Aromatics

COMPANY IDENTITY:  Cascade Designs, INC.			DATE: 08/16/04

PRODUCT IDENTITY:  MSR Superfuel  				PAGE 5 OF 7

REVISION DATE: 11/02/2004                                 SUPERCEDES: 11/28/2001?

LF0001            SECTION 11. TOXICOLOGICAL INFORMATION (CONTINUED)

MATERIAL                                CAS #     CEILING     STEL (OSHA/ACGIH)

LIGHT HYDROTREATED DISTILLATE       68410-97-9     None Known    5.3E3 ppm

ACUTE HAZARDS

EYE & SKIN CONTACT:

Primary irritation to skin, defatting, dermatitis.

Primary irritation to eyes,redness,tearing,blurred vision.

Liquid can cause eye irritation. Wash thoroughly after handling.

INHALATION:

Anesthetic. Irritates respiratory tract. Acute overexposure

can cause serious nervous system depression. Vapor harmful.

Acute overexposure can cause damage to kidneys,blood,nerves,liver & lungs.

SWALLOWING:

Harmful or fatal if swallowed.

Swallowing can cause abdominal irritation, nausea, vomiting & diarrhea.

SUBCHRONIC HAZARDS/CONDITIONS AGGREVATED

CONDITIONS AGGREVATED

Chronic overexposure can cause damage to kidneys,blood,nerves,liver & lungs.

Persons with severe skin,liver or kidney problems should avoid use.

CHRONIC HAZARDS

CANCER, REPRODUCTIVE & OTHER CHRONIC HAZARDS:

Leukemia been reported in humans from Benzene.

This product contains less than 50 ppm of Benzene.

Not considered hazardous in such low concentrations.

Absorption thru skin may be harmful.

COMPANY IDENTITY:  Cascade Designs, INC.			DATE: 08/16/04

PRODUCT IDENTITY:  MSR Superfuel  				PAGE 6 OF 7

REVISION DATE: 11/02/2004                                 SUPERCEDES: 11/28/2001?

SECTION 12. ECOLOGICAL INFORMATION

MAMMALIAN INFORMATION:

No mammalian information is available on this product.

AQUATIC ANIMAL INFORMATION:

The most sensitive known aquatic group to any component of this product is:

Fish are adversely affected by

components of this product.

MOBILITY

This material is a mobile liquid.

DEGRADABILITY

This product is nonbiodegradable.

ACCUMULATION

This product does not accumulate or biomagnify in the environment.

SECTION 13. DISPOSAL CONSIDERATIONS

Recycle / dispose of observing national, regional, state, provincial and local

health, safety & pollution laws.

If questions exist, contact the appropriate agencies.

SECTION 14. TRANSPORT INFORMATION

IF CONTAINER HAS > PRODUCT RQ (SEE SECTION 15) PUT "RQ," BEFORE SHIPPING NAME.

DOT SHIPPING NAME: Petroleum Distillates,n.o.s.,3,UN1268,PG-II

DRUM LABEL:        (FLAMMABLE LIQUID)

IATA / ICAO:       Petroleum Distillates,n.o.s.,3,UN1268,PG-II

IMO / IMDG:        Petroleum Distillates,n.o.s.,3,UN1268,PG-II

EMERGENCY RESPONSE GUIDEBOOK NUMBER:  128

LF0001                 SECTION 15. REGULATORY INFORMATION

EPA REGULATION:

SARA SECTION 311/312 HAZARDS: Acute Health, Fire

All components of this product are on the TSCA list.

SARA Title III Section 313 Supplier Notification

This product contains the indicated <*> toxic chemicals subject to the

reporting requirements of Section 313 of the Emergency Planning & Community

Right-To-Know Act of 1986 & of 40 CFR 372. This information must be

included in all MSDSs that are copied and distributed for this material.

COMPANY IDENTITY:  Cascade Designs, INC.			DATE: 08/16/04

PRODUCT IDENTITY:  MSR Superfuel  				PAGE 7 OF 7

REVISION DATE: 11/02/2004                                 SUPERCEDES: 11/28/2001?

LF0001             SECTION 15. REGULATORY INFORMATION (CONTINUED)

SARA TITLE III INGREDIENTS              CAS#      WT. % (REG. SECTION)   RQ(LBS)

LIGHT HYDROTREATED DISTILLATE       68410-97-9    >95 (311,312)             None

STATE REGULATIONS:

THIS PRODUCT MEETS REQUIREMENTS OF SOUTHERN

CALIFORNIA AQMD RULE 443.1 & SIMILAR REGULATIONS

INTERNATIONAL REGULATIONS

The components of this product are listed on the chemical

inventories of the following countries:

Australia, Canada, Europe (EINECS), Japan, Korea, United Kingdom.

SECTION 16. OTHER INFORMATION

HAZARD  RATINGS:

HEALTH (NFPA): 1,    HEALTH (HMIS): 1,    FLAMMABILITY: 3,    REACTIVITY: 0

This information is intended solely for the use of individuals

trained in the NFPA & HMIS hazard rating systems.

EMPLOYEE TRAINING

Employees should be made aware of all hazards of this material (as stated

in this MSDS) before handling it.

NOTICE

The supplier disclaims  all expressed  or implied warranties of merchantability

or fitness for a specific use,  with respect to the product  or the information

provided herein, except for conformation to contracted specifications.

All information appearing herein is based upon data obtained from manufacturers

and/or recognized technical sources.  While the information  is believed to be

accurate, we make no representations as to its accuracy or sufficiency.

Conditions of use are beyond our control,  and therefore  users are responsible

for verifying  the data  under their  own  operating  conditions  to determine

whether the product is suitable  for their particular purposes  and they assume

all  risks of  their use,  handling,  and disposal  of the product.  Users also

assume all risks  in regards  to the publication  or use of,  or reliance upon,

information contained herein.

This information relates only  to the product  designated herein, and does not

relate to its use in combination with any other material or process.

Unless updated, this Material Safety Data Sheet is valid until 08/16/2007?.

Zen Backpacking Stoves